## Slide 1: 9th International Conference on Computing, Communication, Control and Automation (ICCUBEA-2025)
Pimpri Chinchwad Education Trust’s
Pimpri Chinchwad College of Engineering, Pune
Presentation By: Kaustubh Warme
PAPER ID - 1006
PAPER TITLE : Vision-Based Safety Monitoring at Construction Sites Using YOLOv8 and Human Pose Estimation
Author Name : Shubhankar Jakate, Chandrakant Thakare, Pratiksha Deshmukh, Kaustubh Warme, Anuradha Yenkikar, Nilesh P. Sable.
BRACT’s Vishwakarma Institute of Information Technology, Pune, India.

## Slide 2: Outline
Abstract
Introduction
Problem Statement and Objectives
Related Work
Methodology
Result/Discussion
Conclusion and Future Scope
1
2
3
4
5
6
7
References
8

## Slide 3: Abstract
Problem
Unsafe worker behavior + Missing Personal Protective Equipment PPE (helmet, mask, vest) → Real-time safety risk on construction sites
Solution
Vision-based Safety Monitor using YOLOv8 + Human Pose Estimation + Real-time PPE Detection
Features
Real-Time , Detects PPE + workers, SORT/ByteTrack integration.
Impact
Real-time PPE + Pose Detection, reduces site accidents | Applications: Construction, Safety, IoT
🎯Detects PPE
⚡Real-time
🎙Multimodal
📑ByteTrack integration

## Slide 4
Introduction
Why safety matters ?
Prevents 60%+ of site accidents caused by missing PPE (OSHA, 2023).
Construction accounts for ~1 in 5 worker deaths globally (ILO, 2023).
Real-time monitoring can cut accident rates by up to 40% (McKinsey, 2024).
Limitations of Existing Safety Monitoring Systems
PPE Detection → finds gear, ignores behavior (Automation in Construction, 2025).
Pose Estimation → tracks movement, weak in real sites (OpenPose, 2025).
Combined Models → separate tasks, miss real-time prevention (FairMOT, 2021).
The Gap
Current systems = separate PPE & pose, static image-based, not real-time.
Need: Integrated, context-aware, real-time safety monitoring.
To address these gaps, we propose our
Vision-Based, Context-Aware Safety Monitoring System.

## Slide 5
Problem Statement
Construction workers face high risks due to unsafe practices and non-compliance with PPE, leading to frequent accidents and fatalities. Existing AI-based safety systems are either limited to PPE detection or posture estimation, making them generic, static, and ineffective in real-world, cluttered site environments. Their lack of integration, contextual awareness, and real-time adaptability prevents accurate risk assessment and proactive accident prevention.
A vision-based, context-aware safety monitoring system can combine PPE detection with human pose estimation to deliver real-time, dynamic safety insights. By leveraging AI-driven recognition, continuous monitoring, and proactive alerts, it can reduce accidents, improve compliance, and enhance worker protection on construction sites.

## Slide 6
Objectives
Enhance Safety & Compliance → Detect and monitor PPE (helmets, masks, vests) to reduce site accidents.
Combine Detection & Behavior → Integrate YOLOv8 object detection with human pose estimation for holistic safety analysis.
Enable Real-Time Monitoring → Deliver fast, accurate insights suitable for dynamic construction environments.
Lay Groundwork for Future → Enable IoT-based alerts and tracking (SORT/ByteTrack) for proactive safety systems.

## Slide 7
Related work
Sr. no. | Paper | Results
[1] | YOLOv5 for PPE Detection Nath et al., 2020 | ~88% accuracy in PPE detection, but focused only on helmets/vests, ignoring worker behavior.
[2] | Pose Estimation in Industrial Safety Zhang et al., 2017 | Accurately detects posture variations, but tested mainly in lab conditions, not real sites.
[3] | SORT / ByteTrack Tracking Bewley et al., 2016; Zhang et al., 2022 | Preserve object identity across frames, but don’t analyze worker safety context.
[4] | YOLOv3 & YOLOv4 Advances Redmon, Bochkovskiy et al. | Improved object detection speed & accuracy, but lacked behavioral analytics.
[5] | Vision + IoT Safety Systems Emerging Work, 2021–2023 | Real-time alerts via camera networks & IoT, but still in early development stage.
Table 1. Literature Survey

## Slide 8
Methodology
Dataset
Construction Site Safety Dataset (10,000 images) from Kaggle via Roboflow
Split: 70% training, 20% validation, 10% testing
Pre-processing: resized (640×640), augmentation (flip, rotation)
Model Architecture
YOLOv8 → PPE & object detection
YOLOv8-Pose → 17 keypoint human pose estimation
(Future scope: tracking with SORT/ByteTrack)
Training Setup
Pretrained weights (Ultralytics), 10 epochs, batch size 32
Optimizer: SGD
Tools: Python, Colab GPU (Tesla T4), OpenCV, Pandas, Matplotlib
Integration
Combines PPE detection + posture analysis → holistic safety monitoring

## Slide 9
Methodology
Fig 1.Workflow

## Slide 10
Implementation details
Output/Review (Transcript + Insights)
Training (10k Images, 70/20/10 Split)
Processing
Preprocessing (Resize 640×640, Augmentation, YOLO format)
Input (Site Images/Videos)
1️⃣ Input Construction site images/videos → Pre-processed (640×640, YOLO format, augmented).
2️⃣ Processing YOLOv8n → Object & PPE detection (helmet, mask, vest). YOLOv8n-pose → Human pose estimation (17 keypoints).
3️⃣ Training Dataset: ~10,000 images (Kaggle + Roboflow). Split: 70% train, 20% validation, 10% test. Optimizer: SGD, Batch size 32, 10 epochs.
4️⃣ Output Detections → Worker + PPE compliance status. Pose estimation → Unsafe behavior indicators. Performance: mAP@0.5 = 0.667, Precision = 0.829.
5️⃣ Tools & Environment Python (Colab GPU: Tesla T4). Libraries: Ultralytics YOLOv8, OpenCV, Pandas, NumPy, Seaborn, Matplotlib.
Fig 2. Implementation Flow

## Slide 11
Results
Fig 3. Per Class Performances
Fig 5. Overall Model Performance Metrices
Fig 6. Confusion Matrix
Fig 4. False Positives vs. True Positives per PPE Class

## Slide 12
Results
Fig 7. Sample output with multiple workers on-site
Fig 8. Sample output showing keypoint detection under occlusion.
Fig 9.Sample prediction output demonstrating object detection and pose estimation on a construction site image.
Fig 10. Sample prediction output: pose estimation results
Fig 11. Sample output with multiple workers on-site

## Slide 13
Proposed Vision-Based Safety Monitoring System → combines YOLOv8 object detection and human pose estimation for comprehensive on-site safety.
Achieved high precision (0.829) and competitive mAP@0.5 (0.667), enabling real-time PPE compliance checks and behavioral risk assessment, outperforming traditional PPE-only systems.
Demonstrated strong potential for reducing construction accidents, improving compliance, and providing scalable, automated safety solutions in dynamic environments.
Future Directions →
Integration with IoT-based alert systems for proactive responses.
Continuous video monitoring with SORT/ByteTrack tracking.
Fine-tuning pose estimation on construction-specific datasets.
Deployment in real-world sites for large-scale validation.
Conclusion

## Slide 14
References
OSHA – Commonly Used Statistics https://www.osha.gov/data/commonstats
YOLOv3: An Incremental Improvement – Redmon & Farhadi (2018) https://arxiv.org/abs/1804.02767
YOLOv4: Optimal Speed and Accuracy – Bochkovskiy et al. (2020) https://arxiv.org/abs/2004.10934
YOLOv5 for PPE Detection – Nath et al. (2020) https://doi.org/10.1016/j.autcon.2020.103085
Realtime Multi-Person 2D Pose Estimation (OpenPose) – Cao et al. (2017) https://arxiv.org/abs/1611.08050
SORT: Simple Online and Realtime Tracking – Bewley et al. (2016) https://doi.org/10.1109/ICIP.2016.7533003
ByteTrack: Multi-Object Tracking – Zhang et al. (2022) https://arxiv.org/abs/2110.06864
Ultralytics YOLOv8 Documentation https://docs.ultralytics.com/models/yolov8/

## Slide 15
Any Questions?
THANK YOU